## Slide 1: Design and Application of Hybrid Classification System on Memory IC Testing
Ong Boon Ping
Tan Chin Gee
Han Dongchou Francis

## Slide 2: Description of Problem
This Program is for the testing of Single Semiconductor Memory Chip
In Memory Chip testing, a number of electronic tests are conducted using the programmable automatic electronic tester.
Electronic testing is used not only to sort out chip failures, its results can also be used to find out the locations of failure inside the array. This will then help to identify the root cause of the failures. For example, the source of the failure could be due to the lithography process prior to the chip testing.
A DRAM chip uses row and column to indicate the array cell position. Hence, it is important to understand whether the failures is coming from the row, column, or individual cell (or combination).

## Slide 3: Complications
Auto-test results can be affected by noise which can affect accuracy.
As part of yield enhancement, the focus is to probe for single bit (SB), row (ROW) and column (COL) failures inside the DRAM chips. The failures may happen as a combination. SB failure is attributed to one memory cell; ROW can be due to Word Line Input failures, COL can be due to Sense Amplifier failures.
Hence, it is hard to predict the nature of failures and currently, most of the verifications are done via manual inspection (after the chip is de-capsuled).

## Slide 4: Proposed Solution
A Data Set comprising chip testing data from 58 tests (58 features) and inspected failing mechanisms (3 classes, namely SB, COL, ROW) has been gathered.
A Hybrid Classification Model is built with a capability to select the best solution presented by three techniques, namely Decision-Tree, Multi-layer Perceptron and SVM.
The Competitive Agent in the model compares the accuracy, feature-to-class correlation and assigns penalty for severe mis-classification according to the Confusion Matrix results.

## Slide 5: Overall Design
The Hybrid Classification Model employs three techniques, namely the Decision Tree, MLP, and SVM.
Random Forest is deployed as an Ensemble technique to improve the performance of the Decision Tree.
The solutions from all techniques finally go through the Competitive Agent so that the optimal solution is selected.
Random Forest
SVM
MLP
Competitive Agent

## Slide 6: Data Set
The input data is in CSV format.
“1” represents test positive and “0” as test negative.
ID is dropped at the beginning.
“SB”,”ROW”,”COL” are inspection results. Other than these columns, the rest are automated test results.
Test and Train split are in ratio of 2:1.
The output classes are formed from the 3 columns from raw data, namely, SB, COL, ROW.

## Slide 7: Data Set – Pre-Process
We performed pre-processing on the following:
  Unique Column – ID is removed
  3 Features – Gallop1, Gallop5, Row-Shift7 removed because there is no variance in the values for the 3 features

## Slide 8: Decision Tree
Analysis:
For DT, we are using the DecisionTreeClassifier to perform multi classification on the data set.
Two parameters are tuned for optimal performance – Best Depth and Best Impurity Decrease. See codes on the right.
Fine tuning is then done again on impurity decrease and min_weight_fraction_leaf based on accuracy.
The model is then passed to the Competitive agent.
for DEPTH in range(20,40,1):
dt = DecisionTreeClassifier(criterion='entropy’, max_depth=DEPTH,random_state=0, min_impurity_decrease=0.0001,min_weight_fraction_leaf=0.001)
dt.fit(X_train, y_train)
#post_pruning
prune_duplicate_leaves(dt)
print(DEPTH,dt.score(X_test, y_test))
if dt.score(X_test, y_test)>max_accuracy:
max_accuracy=dt.score(X_test, y_test)
best_depth=DEPTH
#prints for tuning the DEPTH - Best DEPTH = 29
print("DEPTH = ", DEPTH)
Code for finding the Best Depth:
Code for finding the Best Impurity Decrease:
for impurity_decrease in range(5,20,1):
dt = DecisionTreeClassifier(criterion='entropy',max_depth=best_depth, random_state=0,min_impurity_decrease=impurity_decrease*0.00001, min_weight_fraction_leaf=0.001)
dt.fit(X_train, y_train)
#post_pruning
prune_duplicate_leaves(dt)
print(best_depth,impurity_decrease,dt.score(X_test, y_test))
if dt.score(X_test, y_test)>max_accuracy:
max_accuracy=dt.score(X_test, y_test)
best_impurity_decrease=impurity_decrease*0.00001

## Slide 9: Decision Tree
Performance - Multi-labels Confusion Matrices
Performance – Classification Report
Parameters Optimization
selected depth: 21
selected best_impurity_decrease: 0.00010000
selected best_weight_fraction_leaf: 0.00080000
Feature Importance
Using entropy to evaluate the tree leave split.
The three most important features are:
Row Shift 2
Column Short Type 2
Gallop 2
Results:
 | SB |  |  | ROW |  |  | COL | 
 | Predicted Negative | Predicted Positive |  | Predicted Negative | Predicted Positive |  | Predicted Negative | Predicted Positive
Actual Negative | 350 | 46 |  | 623 | 14 |  | 787 | 4
Actual Positive | 17 | 618 |  | 17 | 377 |  | 20 | 220
 | Precision | Recall | F1-score | Support
SB | 0.93 | 0.97 | 0.95 | 635
ROW | 0.96 | 0.96 | 0.96 | 395
COL | 0.98 | 0.92 | 0.95 | 240
Micro avg | 0.95 | 0.96 | 0.95 | 1269
Macro avg | 0.96 | 0.95 | 0.95 | 1269
Weighted avg | 0.95 | 0.96 | 0.95 | 1269
Samples avg | 0.94 | 0.92 | 0.93 | 1269

## Slide 10: Random Forest
Analysis:
Using the Decision Tree Model earlier, using best depth, best impurity decrease as guideline, build the random forest model.
Choosing max_depth of sklearn random forest to 15 layer more than the best depth found in the single decision tree. This will allow more randomness.
Since there are 3000 entries in the dataset, number of tree should in range of 32 to 512. Looping the values of [32,64,128,256,512] to get the best number of tree for the random forest model.
Pruning is not done on the decision trees to allow more randomness.
#Allow more randomness at random forest. Allow tress to grow deeper.
max_depth=best_depth+15
if max_depth>50:
max_depth=50
best_num_tree=32
max_score=0
score_arr=[]
for num_trees in [32,64,128,256,512]:
dt=eval("RandomForestClassifier(bootstrap=True, class_weight=None, criterion='entropy',\
max_depth=%s, max_features='auto', max_leaf_nodes=None,\
min_impurity_decrease=%s, min_impurity_split=None,\
min_samples_leaf=1, min_samples_split=2,\
min_weight_fraction_leaf=%s, n_estimators=%s, n_jobs=None,\
oob_score=False, random_state=0, verbose=0, warm_start=False)" % (max_depth,best_impurity_decrease,best_weight_fraction_leaf,num_trees) )
dt.fit(X_train, y_train)
if dt.score(X_test, y_test)>max_score:
max_score=dt.score(X_test, y_test)
best_num_tree=num_trees
score_arr.append(dt.score(X_test, y_test))
Code for finding the Best Number of Tree:

## Slide 11: Random Forest
Analysis:
The accuracy peaks around 128.
Due to dataset size of 3K entries, large tree number may not improve the accuracy since it reduce the sample size in each tree.
Low tree number may also give unstable behaviour.

## Slide 12: Random Forest
Performance - Multi-labels Confusion Matrices
Performance – Classification Report
Parameters Optimization
Number of tree: 128
max depth: 21+15=36 (additional 15 to increase the randomness. Not going beyond since not all 58 features are having equal significance.)
best_impurity_decrease: 0.00010000
best_weight_fraction_leaf: 0.00080000
Feature Importance
Using entropy to evaluate the tree leave split.
The three most important features are:
Row Shift 2
Column Short Type 2
Gallop 2
Results:
 | SB |  |  | ROW |  |  | COL | 
 | Predicted Negative | Predicted Positive |  | Predicted Negative | Predicted Positive |  | Predicted Negative | Predicted Positive
Actual Negative | 392 | 4 |  | 623 | 14 |  | 788 | 3
Actual Positive | 10 | 625 |  | 10 | 384 |  | 22 | 218
 | Precision | Recall | F1-score | Support
SB | 0.99 | 0.98 | 0.99 | 635
ROW | 0.96 | 0.97 | 0.97 | 394
COL | 0.99 | 0.91 | 0.95 | 240
Micro avg | 0.98 | 0.97 | 0.97 | 1269
Macro avg | 0.98 | 0.96 | 0.97 | 1269
Weighted avg | 0.98 | 0.97 | 0.97 | 1269
Samples avg | 0.94 | 0.93 | 0.93 | 1269

## Slide 13: MLP
Bayesian Hyperparameters Optimization
For MLP, we are tuning seven parameters:
Activation function for the hidden layer (Activation)
L2 penalty (Alpha)
Number of neurons in the 1st hidden layer (Neurons)
Learning rate schedule for weight updates (Learning rate)
Initial learning rate (Initial)
Exponent for inverse scaling learning rate (Exponent)
Solver for weight optimization (Solver)
We used an informed search technique to search through the state space of these seven parameters. This technique utilizes a Bayesian approach of progressively updating its beliefs on the best hyperparameter combination. We implemented the technique using the Hyperopt package.
The state space for each of the seven parameter:
Activation: logistic, tanh, relu, identity
Alpha: float between 0.001 to 1000
Neurons: integer between 1 to 55 (i.e., number of features)
Learning rate: constant, invscaling, adaptive
Initial: float between 0.001 to 0.99
Exponent: float between 0.01 to 0.99
Solver: lbfgs, sgd, adam
ADDITIONAL EXPERIMENTS
1. Does adding a 2nd layer increase accuracy?
We used a randomized grid search to search through the state space of all 3025 combinations of 55 neurons in 1st and 2nd layers. If 1% of these combinations i.e., 30 gives the best accuracy, we only need to run 425 searches to guarantee at least 99% of obtaining one of the 30 best combinations.
We found that adding a 2nd layer didn’t increase model accuracy.
Note: We commented out these codes in the submitted documents because of the long training time required to run the codes
2. Does combining a few estimators to form an ensemble estimator increase accuracy?
We used the scikit-learn function VotingClassifer to combine the top five MLP classifiers into an ensemble estimator.
We found that the ensemble estimator didn’t increase model accuracy.
Analysis:

## Slide 14: MLP
Performance - Multi-labels Confusion Matrices
Performance – Classification Report
Bayesian Hyperparameters Optimization
The best accuracy (0.95) was obtained by setting the hyperparameter values to:
Activation = relu
Alpha = 5.09
Neurons = 9
Learning rate = constant
Initial = 0.52
Exponent = 0.48
Solver = lbfgs
Feature Importance
We used the eli5 packages to determine feature importance through observing how randomizing the value of a feature affects accuracy. A feature that is important to the prediction of the model will cause accuracy to drop if its value is randomizes.
The three most important features are:
Amplifier 1
Column Short Type 2
Column Short Type 3
Results:
 | SB |  |  | ROW |  |  | COL | 
 | Predicted Negative | Predicted Positive |  | Predicted Negative | Predicted Positive |  | Predicted Negative | Predicted Positive
Actual Negative | 141 | 255 |  | 775 | 16 |  | 595 | 42
Actual Positive | 0 | 635 |  | 102 | 138 |  | 23 | 371
 | Precision | Recall | F1-score | Support
SB | 0.71 | 1.00 | 0.83 | 635
ROW | 0.90 | 0.57 | 0.70 | 240
COL | 0.90 | 0.94 | 0.92 | 394
Micro avg | 0.79 | 0.90 | 0.84 | 1269
Macro avg | 0.84 | 0.84 | 0.82 | 1269
Weighted avg | 0.81 | 0.90 | 0.83 | 1269
Samples avg | 0.79 | 0.84 | 0.80 | 1269

## Slide 15: SVM
For SVM, we are using the Radial Basis Function (RBF) kernel. Two parameters have some levels of effect on the results, and they are the gamma and C.
The gamma parameter defines how far the influence of a single training example reaches, with low values meaning ‘far’ and high values meaning ‘close’. The gamma can be seen as the inverse of the radius of influence of samples selected by the model as support vectors.
The C parameter trades off correct classification of training examples against maximization of the decision function’s margin. Larger values of C means that a smaller margin will be accepted. A lower C gives a larger margin. This would mean a simpler decision function, but it erodes training accuracy. Hence C is like a regularization parameter in the SVM.
The program runs thru different permutations of gamma and C using nested While and For loops. The optimal values of gamma and C are then established.
while gamma_value < 10:
for C_val in range(1,10,1):
svm=OneVsRestClassifier( SVC(kernel="rbf", gamma=gamma_value, C=C_val) )
svm.fit(X_train, y_train)
predictions = svm.predict(X_test2)
if svm.score(X_train, y_train) > max_score:
max_score = svm.score(X_train, y_train)
optimal_C = C_val
optimal_gamma = gamma_value
from sklearn.metrics import classification_report, confusion_matrix
print("C= ", C_val)
print("gamma= ", gamma_value)
print(multilabel_confusion_matrix(y_test,predictions))
print(classification_report(y_test,predictions))
print("Accuracy on training set: {:.3f}".format(svm.score(X_train, y_train)))
print("Accuracy on test set: {:.3f}".format(svm.score(X_test2, y_test)))
print("============================================")
gamma_value = gamma_value + 0.01
The program:
Analysis:

## Slide 16: SVM
Performance - Multi-labels Confusion Matrices
Performance – Classification Report
SVM Hyperparameters Optimization
The best accuracy (0.984 on Training and 0.942 on Test) was achieved and doesn’t improve beyond the following parameter settings:
C = 4
Gamma = 0.11
Results:
 | SB |  |  | ROW |  |  | COL | 
 | Predicted Negative | Predicted Positive |  | Predicted Negative | Predicted Positive |  | Predicted Negative | Predicted Positive
Actual Negative | 382 | 14 |  | 617 | 20 |  | 773 | 18
Actual Positive | 0 | 635 |  | 5 | 389 |  | 13 | 227
 | Precision | Recall | F1-score | Support
SB | 0.98 | 1.00 | 0.99 | 635
ROW | 0.95 | 0.99 | 0.97 | 394
COL | 0.93 | 0.95 | 0.94 | 240
Micro avg | 0.96 | 0.99 | 0.97 | 1269
Macro avg | 0.95 | 0.98 | 0.96 | 1269
Weighted avg | 0.96 | 0.99 | 0.97 | 1269
Samples avg | 0.93 | 0.94 | 0.93 | 1269

## Slide 17: Competitive agent
The Competitive Agent gives a score to each technique, namely, Decision Tree, MLP, SVM based on feature correlation and accuracy.
Based on the Confusion Matrices, the total False Positive for ROW, COL and SB will determine the need for retraining.
In terms of Retraining:
  For Random Forest, it will repeat with added number of trees
  For MLP and SVM, it will repeat with bagging (#estimator = 10)
If the retrained model is having better accuracy, it will replace the existing model. Retraining chance is set once since the model should not need much improvement at this stage.

## Slide 18: Voting Ensemble
After completing re-training after competition, the three models will be used for voting ensemble.
We use the Voting Classifier in which the ensemble model makes the prediction by majority vote.
This is expected to help in situations where different models are giving different predictions for a particular class.

## Slide 19: Voting Ensemble
SVM is giving highest overall score compared to MLP and random forest. However, SVM tends to give better accuracy on SB class but not in COL and ROW class. This can be due to the nature of the hyperplane which may give more bias as a result.
MLP has better score in ROW and COL.
Random forest is giving lower score but is able to produce high accuracy in prediction. This can be improved if there is more data and so that the number of trees can be increased.

## Slide 20: Voting Ensemble
Random forest SB score: 0.9903006789524733
Random forest COL score: 0.9844810863239574
Random forest ROW score: 0.9844810863239574
Overall Random Forest Score0.9598023981818824:
SVM SB score: 0.997090203685742
SVM COL score: 0.9844810863239574
SVM ROW score: 0.9844810863239574
Overall svm Score0.9663828259852841:
MLP SB score: 0.9941804073714839
MLP COL score: 0.98545101842871
MLP ROW score: 0.98545101842871
Overall Winner MLP Score 0.9654622235356315
Voting System SB score
0.994180407
Voting System COL score
0.985521018
Voting System ROW score
0.985751018

## Slide 21: Voting Ensemble
The overall voting accuracy of 96.58% is not as high as compared to the highest score of 96.63% in SVM.
However, voting accuracy on ROW/COL classes increases if compared to any single model.
Hence, voting ensemble still helps in certain features.

## Slide 22: Conclusion
The final voting ensemble system using random forest, SVM and MLP are able to give high accuracy prediction (96.5% for overall, 99.4% for SB, 98.5% for COL/ROW classes).
This pertains to a trade-off concerning the SB feature, with greater prediction accuracy on the ROW and COL.
We consider this application successful in regards to the requirements of the project.